## Slide 1: Arbor Basin: how the system is operated
ArborBasin.mdl (RiverWare 9.4)
Run 2018-01-01 to 2019-01-01, timestep 1 DAY
41 simulation objects: 11 WaterUser, 7 Reach, 4 LevelPowerReservoir, +10 more types
2026-08-28
Structure, operating policy, and one year of simulated results
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl.
Counts and run horizon are read from the model header.

## Slide 2: What this deck covers
- The physical system: two basins joined by one transbasin diversion
- The operating policy: nine rule groups, west basin to east basin
- The decision levers an external workflow can move
- Simulated results for calendar year 2018
ArborBasin.mdl | 2026-08-28

## Slide 3: West basin: a five-reservoir cascade
- Aspen through Elm, four of them power reservoirs. The Transbasin Diversion at Cedar is the only water leaving this basin.
Aspen
Dogwoo...
Aspen...
Birch
Birch...
Cedar
Cedar...
Transb...
Dogwood
Reach...
Dogwoo...
Elm
Easter...
Diversion
Power reservoir / plant
Reach
Storage reservoir
Water user
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl. 13 objects, 13 flow links and 2 data links. Link direction is inferred from which end is an inflow slot; data and head links are dashed.
Dashed edges are data and head links, not water: Aspen's tailwater is linked to Birch's pool elevation, and Dogwood's to Elm's. Drawn as a subset of the 41-object network; the whole model on one slide is not readable when projected.

## Slide 4: East basin: Hickory and the irrigation complex
- The transbasin water arrives above Hickory, which supplies Juniper, the interstate minimum flow, and the Linden and Mulberry canals.
Gage Abo...
Linden I...
Transbas...
Hickory
Hickory...
Juniper...
Intersta...
Juniper...
Linden C...
Linden G...
Mulberry...
Mulberry...
Mulberry...
Mulberry...
Mulberry...
Mulberry...
Canal
Confluence
Diversion
Groundwater
Power reservoir / plant
Reach
Storage reservoir
Stream gage
Water user
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl. 16 objects, 16 flow links and 4 data links. Link direction is inferred from which end is an inflow slot; data and head links are dashed.
Aggregate sites are drawn as single nodes; their districts are separate objects in the model. The two groundwater objects exchange water laterally and are recharged by canal seepage and irrigation returns.

## Slide 5: The six reservoirs the policy operates
- Every rule group below is named for one of these reservoirs.
41 objects: 11 WaterUser, 7 Reach, 4 LevelPowerReservoir, 3 AggDiversionSite, 3 DistributionCanal, 2 AggDistributionCanal, +7 more types
Object | Type | Slots | Description
Aspen | LevelPowerReservoir | 127 | Top reservoir of the west-basin power cascade. Its tailwater is set by Birch's pool ele...
Birch | LevelPowerReservoir | 125 | Second power reservoir in the west cascade, between Aspen and Cedar. Its pool elevation...
Dogwood | LevelPowerReservoir | 127 | Power reservoir below Cedar that also diverts directly to Dogwood Irrigation. Its tailw...
Elm | LevelPowerReservoir | 126 | Bottom reservoir of the west cascade. It is operated to a Pool Elevation Target rather...
Cedar | StorageReservoir | 32 | Storage workhorse of the west basin and the source of the transbasin diversion. Its Div...
Hickory | StorageReservoir | 37 | Storage reservoir at the head of the east basin, fed by the Gage Above Hickory inflow p...
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl, object inventory. 6 of 6 objects listed.

## Slide 6: West basin, upper cascade: operate, then protect
Rule set "Arbor Basin Rules (from MRM run)", agenda order ASCENDING -- the bottom rule fires first, and a rule listed higher fires later and overrides it.
Operating policy for the Arbor Basin: hold each reservoir between its elevation limits, operate the west cascade to guide curves and targets, move water east through the transba...
# | Group and rules | What it does
 | Aspen Rules | Draws the pool toward the monthly guide curve, then overrides that if a limit is crossed.
31 | Aspen Elevation Max | Increases the release when the pool would exceed its maximum.
32 | Aspen Elevation Min | Cuts the release when the pool would fall below its minimum.
33 | Aspen Outflow Min | Floors the release at the minimum outflow.
34 | Aspen Operate to Guide Curve | The base operation: release to move the pool toward the Elevation Guide Curve.
35 | Cause Sporadic Error | A deliberate tripwire: aborts the run when Cedar's Diversion Min Elevation is out of range.
 | Birch Rules | The same pattern one reservoir down, with an outflow target as the base operation.
27 | Birch Elevation Max | Increases the release when the pool would exceed its maximum.
28 | Birch Elevation Min | Cuts the release when the pool would fall below its minimum.
29 | Birch Outflow Min | Floors the release at the minimum outflow.
30 | Birch Outflow Target | The base operation: release to the target outflow.
ArborBasin.mdl | 2026-08-28
Notes: Source: rule set "Arbor Basin Rules (from MRM run)" as stored in ArborBasin.mdl. Numbers are agenda positions, not execution order for ASCENDING sets.
Agenda order is ASCENDING, so within a group the rule listed last fires first and the elevation limits, listed first, take final priority.

## Slide 7: The hinge: what the west basin can spare
Rule set "Arbor Basin Rules (from MRM run)", agenda order ASCENDING -- the bottom rule fires first, and a rule listed higher fires later and overrides it.
Operating policy for the Arbor Basin: hold each reservoir between its elevation limits, operate the west cascade to guide curves and targets, move water east through the transba...
# | Group and rules | What it does
 | Transbasin Diversion | Decides how much water leaves the west basin for the east.
26 | Cedar Available for Diversion | Offers the storage above Cedar's Diversion Min Elevation, plus inflow, less the required minimum outflow.
 | Cedar Rules | Operates the west basin's storage workhorse to its monthly guide curve.
22 | Cedar Elevation Max | Applies the maximum from the Pool Elevation Limits table.
23 | Cedar Elevation Min | Applies the minimum from the Pool Elevation Limits table.
24 | Cedar Outflow Min | Floors the release at the minimum outflow.
25 | Cedar End of Month Guide Curve | Solves for guide-curve storage on the last day of the month, and walks toward it on other days.
 | Dogwood Irrigation | Computes west-basin irrigation availability the same way, gated by Dogwood's own floor.
21 | Dogwood Available for Diversion | Offers the storage above Dogwood's Diversion Min Elevation to its irrigation diversion.
ArborBasin.mdl | 2026-08-28
Notes: Source: rule set "Arbor Basin Rules (from MRM run)" as stored in ArborBasin.mdl. Numbers are agenda positions, not execution order for ASCENDING sets.
Cedar.Diversion Min Elevation and Cedar.Pool Elevation Limits are scalar slots written before a run by the input DMIs.

## Slide 8: East basin: senior rights come first
Rule set "Arbor Basin Rules (from MRM run)", agenda order ASCENDING -- the bottom rule fires first, and a rule listed higher fires later and overrides it.
Operating policy for the Arbor Basin: hold each reservoir between its elevation limits, operate the west cascade to guide curves and targets, move water east through the transba...
# | Group and rules | What it does
 | Hickory Rules | The east basin's water-rights logic. The firing order is the policy.
6 | Hickory Elevation Max | Increases the release when the pool would exceed its maximum.
7 | Hickory Elevation Min | Cuts the release when the pool would fall below its minimum.
8 | Hickory Elevation Min Reduce Diversion | Cuts the diversion further when the pool is below its minimum.
9 | Reduce Hickory Diversion | Cuts the canal supply to Linden and Mulberry in favour of Juniper's senior rights.
10 | Supplement Juniper from Hickory Storage | Releases stored water for Juniper, but only while the pool is above its supplement threshold.
11 | Hickory Pass Natural Flows for Juniper and Interstate | Passes the natural flow arriving above the reservoir, up to what Juniper and the interstate minimum need.
12 | Interstate Flow Requirement | Reserves the interstate minimum first, by setting the Juniper Diversion's minimum bypass.
ArborBasin.mdl | 2026-08-28
Notes: Source: rule set "Arbor Basin Rules (from MRM run)" as stored in ArborBasin.mdl. Numbers are agenda positions, not execution order for ASCENDING sets.
Hickory.Pool Elevation Min to Supplement Irrigation is the scalar threshold in the supplement rule, and is DMI-written.

## Slide 9: Lower cascade: the same two safeguards
Rule set "Arbor Basin Rules (from MRM run)", agenda order ASCENDING -- the bottom rule fires first, and a rule listed higher fires later and overrides it.
Operating policy for the Arbor Basin: hold each reservoir between its elevation limits, operate the west cascade to guide curves and targets, move water east through the transba...
# | Group and rules | What it does
 | Dogwood Rules | The safeguard pattern only: floors and ceilings, no separate base operation.
18 | Dogwood Elevation Max | Increases the release when the pool would exceed its maximum.
19 | Dogwood Elevation Min | Cuts the release when the pool would fall below its minimum.
20 | Dogwood Outflow Min | Floors the release at the minimum outflow.
 | Elm Rules | The bottom reservoir of the cascade, with a pool elevation target and a flood release rule.
13 | Elm Elevation Max | Increases the release when the pool would exceed its maximum.
14 | Elm Elevation Min | Cuts the release when the pool would fall below its minimum.
15 | Elm Outflow Min | Floors the release at the minimum outflow.
16 | Elm Pool Elevation Target | The base operation: release toward the target pool elevation.
17 | Elm Required Spill | Makes the flood release when one is required.
ArborBasin.mdl | 2026-08-28
Notes: Source: rule set "Arbor Basin Rules (from MRM run)" as stored in ArborBasin.mdl. Numbers are agenda positions, not execution order for ASCENDING sets.
Both groups call the three shared functions in the set's utility group: OutflowForMinOutflowRules, OutflowForMinElevationRules, OutflowForMaxElevationRules.

## Slide 10: Post-processing: what the run reports
Rule set "Arbor Basin Rules (from MRM run)", agenda order ASCENDING -- the bottom rule fires first, and a rule listed higher fires later and overrides it.
Operating policy for the Arbor Basin: hold each reservoir between its elevation limits, operate the west cascade to guide curves and targets, move water east through the transba...
# | Group and rules | What it does
 | Post-processing | Fires last, and writes the system-wide summary slots nothing else reads.
1 | Energy Cumulative | Accumulates each power object's energy over the run.
2 | System Spill | Sums spill volume across the reservoirs.
3 | System Depletion Shortage | Sums depletion shortage across the water users.
4 | System Energy | Sums energy across the power objects into System Data.
5 | Interstate Flow Requirement Violation | Records any shortfall below the interstate minimum flow.
ArborBasin.mdl | 2026-08-28
Notes: Source: rule set "Arbor Basin Rules (from MRM run)" as stored in ArborBasin.mdl. Numbers are agenda positions, not execution order for ASCENDING sets.
These write the System Data slots the output DMIs export after a run: Total Energy, the west- and east-basin irrigation totals, Total Spill Volume, Total Transbasin Diversion, and Total Depletion Shortage.

## Slide 11: The levers an external workflow moves
- Cedar.Diversion Min Elevation - the floor below which the transbasin diversion is cut off
- Cedar.Pool Elevation Limits - the adjustable maximum and minimum operating elevations
- Dogwood.Diversion Min Elevation - the floor for west-basin irrigation access
- Hickory.Pool Elevation Min to Supplement Irrigation - how deeply east-basin storage is drawn for irrigation
- Input DMIs write these before a run; output DMIs export the System Data totals after it.
ArborBasin.mdl | 2026-08-28
Notes: All four are scalar slots on the objects named. The DMIs are listed in the model's DMI catalog: ArborInputDMI, ArborMRMInputs, From Borg-RiverWare, and their output counterparts.

## Slide 12: Simulated pool elevations, 2018
- One reservoir from each part of the story: the two power reservoirs at the top, Cedar at the hinge, and Hickory in the east.
Chart: m
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl, stored results for Aspen.Pool Elevation (m), Birch.Pool Elevation (m), Cedar.Pool Elevation (m), Hickory.Pool Elevation (m). 2018-01-01 to 2019-01-01, 366 points. Gaps are timesteps with no stored value.
All four are in metres, so the four traces share one value axis. The elevation ranges differ by more than 100 m, which is why the lower reservoirs look flat.

## Slide 13: What actually crossed the divide
- Cedar's release, the transbasin diversion it feeds, and what Hickory passed downstream.
Chart: cms
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl, stored results for Cedar.Outflow (cms), Transbasin Diversion.Outflow (cms), Hickory.Outflow (cms). 2017-12-28 to 2019-01-01, 370 points. Gaps are timesteps with no stored value.
All three are flows in cms. The transbasin series is the outflow of the Transbasin Diversion object, which enters the east basin above Hickory.

## Slide 14: Reading this deck
- Every figure here comes from the model file itself; nothing is inferred beyond it.
- Result series are the values stored in the model when it was saved, not a fresh run.
- Rule behaviour is summarised. RiverWare's Rule Log is the authority on what actually fired.
- Check any number against RiverWare before it informs a decision.
- Arbor Basin is the CADSWES training model, not an operating model of a real basin.
ArborBasin.mdl | 2026-08-28
Notes: Source: ArborBasin.mdl.